## Slide 1
Instrumentation and Control
CSE 325
Mehedi Hasan
Lecturer
Computer Science and Engineering(CSE)
Daffodil International University(DIU)
We are all in the gutter, but some of us are looking at the stars.
-Oscar Wilde

## Slide 2
Signal Conditioning Systems
Signal conditioning refers to operations performed on signals to convert to a suitable for interfacing with other elements in the instrumentation process.
 The raw signal may:
 be too small – have to be amplified
 contain noise – have to be removed
 be non-linear – need linearization
 be analog – have to make digital
 be digital – have to make analog
 be hazardous – require isolation
The conditioned signal is then transferred to the output stage (for indication, recording, logging etc.) which provides the value corresponding to the measurand.

## Slide 3
Elements of Signal Conditioning System
The following are some of the processes that can occur in conditioning a signal:
 Conversion – getting the signal into the right type of signal
 Change of signal level – getting the level of the signal right
 Eliminating or reducing noise – increasing the signal-to-noise ratio (SNR)
 Linearization – making the output linear of the measurand
 Impedance/load matching – for proper power coupling
 Protection – to prevent damage to the next element/component

## Slide 4
Conversion – getting the signal into the right type of signal
Analog to Digital and Digital to Analog Converters
Threshold Digitization
It is sufficient to use a threshold comparator which will then produce a digital output.
Output from magnetic pick-up circuit varies from 100 mV to 150 mV (for example).
The threshold is set by the resistors to 0.13V.
The output is zero until the voltage on the (+) input rises above the threshold.
When the input dips below 0.13V the output goes back to zero.

Now, each pulse represents a rotation of the rotor. Counting the pulses in a given time can give the speed of rotation of the rotor or other data (e.g. flow rate)

## Slide 5
Analog to Digital Conversion
Converts analog signals into binary numbers/words
Why the conversion:
Processing by a computer or by logic circuits, including arithmetic operations, comparison, sorting, ordering, and code conversion
Storage on electronic media until ready for further handling
Display in numerical or graphical form on a computer/other digital device
Digital transmission for less error

## Slide 6
Analog to Digital Conversion
Where do we use an ADC?

## Slide 7
Analog to Digital Conversion
Steps in A/D Conversion:
Analog signal: continuous in time and magnitude
Sampled signal: discrete in time but can be of any magnitude
Quantized signal: discrete in magnitude
Digital signal: coded quantized signal

## Slide 8
Analog to Digital Conversion : Sampling
Sampling converts analog signal (continuous in time and magnitude) into discrete time signal (discrete in time but can have any magnitude)
The intervals, ts , must be carefully chosen to ensure an accurate representation of the original analogue signal.

## Slide 9
Analog to Digital Conversion : Sampling
The problem of losing information in the sampling process, it is necessary to recall Shannon’s information theorem and Nyquist’s criteria.
Shannon’s information theorem states the following.
• An analogue signal with a bandwidth of fa must be sampled at a rate of fs > 2fa
To avoid loss of information.
• The signal bandwidth may extend from d.c. to fa or from f1 to f2, where fa = f2 − f1
The Nyquist criterion is as follows.
• If fs < 2fa, then a phenomenon called aliasing will occur.
To avoid aliasing and loss of information, sampling frequency must be at least twice the highest frequency of the signal.

## Slide 10
Analog to Digital Conversion : Sampling
The signals in the above figure were sampled with the frequency fs > 2w.

## Slide 11
Analog to Digital Conversion : Sampling
Aliasing is the distortion caused when a signal is sampled below the Nyquist rate, resulting in overlap of frequency components.
If fs < 2fa, the replicated signal bands interfere mutually and a distorted signals appear at the output. This effect is called aliasing.
Anti-aliasing filter: An anti-aliasing low-pass filter is used before sampling to limit the signal bandwidth to the Nyquist frequency , thus preventing aliasing.

## Slide 12
Analog to Digital Conversion : Quantization
Quantization is breaking down the values of the sampled signal into a set of finite number of quantized values
Example:
We have 0-10V signals. Separate them into a set of discrete states with 1.25V increments. (How did we get 1.25V?)
Quantizer Output States
The number of output levels (states) in a quantizer is:
where:
= number of bits in A/D converter
Example
For a 3-bit ADC:
So, there are 8 quantization levels Quantization Step Size (q)
It is the difference between two adjacent levels

## Slide 13
Analog to Digital Conversion : Encoding
Encoding is the process of converting quantized values into binary (digital) form.
A unique digital number/word is assigned to each of the quantized states

## Slide 14
Analog to Digital Conversion : Transfer characteristics
From Fig (a) we can see that the quantization error is varying between 0 and q Value.
Usually the characteristic of the quantization is shifted by the q/2 value thus the error of quantization is varying between –q/2 and +q/2 (Fig. b).

## Slide 15
Analog to Digital Conversion : Transfer characteristics