## Slide 1
Instrumentation and Control
CSE 325
Mehedi Hasan
Lecturer
Computer Science and Engineering(CSE)
Daffodil International University(DIU)
Still climbing after knowledge infinite, And always moving as the restless spheres
-Tamburlaine The Great by Christopher Marlowe

## Slide 2
The Transfer Function
A transfer function is a mathematical way to describe how a control system transforms an input into an output.
Definition
In control systems, the transfer function is defined as:
where:
= Laplace transform of the output
= Laplace transform of the input
= complex frequency variable (assuming zero initial conditions)
Knowledge that you have to remember:
Laplace Transform of Differentiation
If L{f(t)} = F(s)
First derivative: L{ df(t)/dt } = sF(s) − f(0)2)
Second derivative: L{ d²f(t)/dt² } = s²F(s) − s f(0) − f’(0)
nth derivative: L{ dⁿf(t)/dtⁿ } = sⁿF(s) − sⁿ⁻¹ f(0) − sⁿ⁻² f'(0) − ... − f⁽ⁿ⁻¹⁾(0)
Under zero initial conditions: L{ df(t)/dt } = sF(s)
L{ d²f(t)/dt² } = s²F(s)
L{ dⁿf(t)/dtⁿ } = sⁿF(s)

## Slide 3
The Transfer Function
Derivation of the Transfer Function
A general th-order linear time-invariant differential equation:
where is the output, is the input, and the coefficients and describe the system.
Taking the Laplace transform of both sides yields:
This is an algebraic equation in . Assuming all initial conditions are zero, Eq. (2.51) simplifies to:

## Slide 4
The Transfer Function
Transfer Function:
This expression separates the output , the input , and the system itself, represented by the rational function in . This ratio is called the transfer function of the system, defined under zero initial conditions.
The output, C(s) by using

## Slide 5
The Transfer Function: Important terms and Procedure
PROCEDURE
The following steps are involved to obtain the transfer function of the given system.
Step 1: Write the differential equations for the given system. Step 2: Take the Laplace transform of the equations obtained in Step 1, assuming all initial conditions are zero. Step 3: Take the ratio of the transformed output to the input. Step 4: The ratio of the transformed output to the input obtained in Step 3 is the required transfer function of the given system.
CHARACTERISTIC EQUATION OF A TRANSFER FUNCTION
The characteristic equation of a linear system can be obtained by equating the denominator polynomial of the transfer function to zero. Thus, the characteristic equation of the transfer function will be

## Slide 6
The Transfer Function: Poles and Zeros
POLES AND ZEROS OF A TRANSFER FUNCTION
The numerator and denominator can be factored into and terms respectively. Then the transfer function can be expressed as
where is known as the gain factor, and is the complex frequency.
POLES: The poles of are those values of that make tend to infinity. For example, we have poles at , , and a pair of poles at
ZEROS: The zeros of are those values of that make tend to zero. For example, we have zeros at , , and a pair of zeros at

## Slide 7
The Transfer Function: Example
PROBLEM 01: Find the transfer function, , corresponding to the differential equation
ANSWER:
PROBLEM 02: Find the differential equation corresponding to the transfer function,
ANSWER:

## Slide 8
The Transfer Function: Electrical Network Transfer Functions

## Slide 9
The Transfer Function: Electrical Network Transfer Functions
PROBLEM: Find the transfer function relating the capacitor voltage , VC(s), to the input voltage, V(s) in Figure
Applying KVL, Summing the voltages around the loop, assuming zero initial conditions, yields the equation for this network as
Changing variables from current to charge using yields
From the voltage-charge relationship for a capacitor in Table 2.3,
Substituting Eq. (2.63) into Eq. (2.62) yields

## Slide 10
The Transfer Function: Electrical Network Transfer Functions
Taking the Laplace transform assuming zero initial conditions, rearranging terms, and simplifying yields
Solving for the transfer function, , we obtain
where is the Laplace transform of the input voltage, and is the Laplace transform of the output voltage across the capacitor.

## Slide 11
The Transfer Function: Electrical Network Transfer Functions
Problem: Find the transfer function of the given network.
Apply KVL in mesh (1)
Apply KVL in mesh (2)
Take Laplace transform of equations with the assumption that all initial conditions are zero.
Calculation of transfer function

## Slide 12
The Transfer Function: Electrical Network Transfer Functions
Problem: Obtain the transfer function for fig.
Answer:
Problem: Find the transfer function of the given network
Answer:

## Slide 13
The Transfer Function: Electrical Network Transfer Functions
Problem: Find the transfer function of the given network
Answer: